Use of HASP-HL-Net key with GRAFIS

Installation at server computer

The HASP-HL-Net key (HASP server) must be connected to one of the computers in your local network (via USB). This computer does not need to be the file server but it must run all the time when users want to use GRAFIS.

When GRAFIS is not installed on the HASP server computer at first the drivers of HASP HL have to be installed (to be found on GRAFIS installation CD, file \GRAFIS\HILFEN\ HASPUserSetup.exe). The software for HASP server can be found in the folder \Tools\HASP-Server on your GRAFIS-CD. The file LMSETUP.EXE must be executed to install HASP server.

For control of current state of HASP server you should also install the monitor program. Therefore you need to execute AKSMON32.EXE (from \Tools\HASP-Server).

Setup of client computers

GRAFIS must be installed normally from the CD to every client computer. It is also possible to create a first installation and use it as a template (simply by copying to the other clients). In this case it is only necessary to install HASP HL drivers by hand (see above).

To make sure the client applications will find HASP HL server, the IP address of the server or the server name must be noted into the file NETHASP.INI (situated in working directory of GRAFIS; typically C:\GRAFIS). It is also allowed to place this file into the Windows folder. For a typical TCP/IP configuration of a network this file contains only the following entries:

[NH_TCPIP]

NH_SERVER_ADDR=127.0.0.1,192.168.1.46

The entry of "127.0.0.1" allows the software to look for a local HASP-HL first. If there is no local key, the software will look for the server key using the address from the second place (and so on). There may be also a server name, e.g.: NH_SERVER_ADDR=luzie

A file with the minimum of entries in a typical TCP/IP network is to be found on the GRAFIS installation CD \Tools\HASP-Server. The same folder also contains a file with complete list of entries that allows a special configuration for special purposes.

In addition to this file the parameter HLSERVER in file GRAFIS.INI must be set correctly. The meaning of its values is:

HLSERVER=0	only local keys are allowed

HLSERVER=1	only network keys are allowed

HLSERVER=2	look for local key first, then look for HASP server